## Slide 1: Multi-view shape reconstruction

## Slide 2: Shape reconstruction
Given
  A set of images (views) of an object / scene
  Camera calibration information
  [Light calibration information]
Find the surface that best agrees with the input images.
…
Approach:
chose a surface representation
define a photo-consistency function
[in practice photo-consistency+regularization]
solve the following minimization

## Slide 3: Photo-consistency function(al)
Based on image cues (shading, stereo, silhouettes, …)
Extension SFS/PS to multi-view:
SFS
Move camera
Move object
PS
Needs camera/light calibration !

## Slide 4: Surface representation
Image-centered
Depth/disparity w.r. to image plane
Image plane
3D point
Voxels
Level sets (implicit)
Mesh
Depth with respect to a base mesh
Local patches
3D plane
Object-centered
time
Partial object reconstr.
Limited resolution
Viewpoint dependent

## Slide 5: Comparison of different methods
2 datasets
No light
(moving camera)

## Slide 6: Volumetric representation
Object : collection of voxels
Normals : ?
Method: carve away voxels that are not photo-consistent with images
(purely discrete)
Regularization: no way of ensuring smoothness
Visibility: ensured by the order of traversal (in general a problem!)

## Slide 7: Disparity/Depth map
Reference image plane
3D point
Reference
image
Object (surface) :
Normals :
Method: find f that best agrees with the input images (minimize the cost functional integrated over the surface)
Regularization: smoothness on
Visibility: ? (mesh defined on image plane + Zbuffering)

## Slide 8: Depth w.r. base mesh
Object (surface) : , d – displacement direction (displacement map)
Normals : local (per triangle) transform to global CS
Method:
Regularization: smoothness on (local / global)
Visibility: ? (fine mesh to connect points on each plane + Zbuffering)
How to deal with boundaries ?

## Slide 9: Mesh
Object (surface) : mesh vertices
Normals : interpolated
Method: move vertices along interpolated normals based on photo-consistency of neighboring triangles.
Regularization: smooth normals
Visibility: Zbuffering
Topologiocal changes ?

## Slide 10: Mixed Representations:Local patches
Mixed approaches :
  patches on voxels for a finer surface representation
  mesh on pre-computed voxel correlation (potential fields)
  [Esteban and Schmitt CVIU 2005]
  (depth on base mesh)
Patches :
  arbitrary : [Zheng, Paris et al. IJCV2006]
  quadratic : surfels [Carceroni and Kutulakos IJCV 2002]

## Slide 11: Optimization
Disparity map
Depth w.r.plane
Level sets
Mesh
Voxels
Discrete
methods
Graph-cuts
Belief propagation
Dynamic programming…
Voxel carving (exhaustive search
For same color)
Continuous
methods
Non-linear optimization
Variational calculus

## Slide 12: Summary
Discrete
Voxel carving
Graph cut techniques
Continuous
Variational and level set techniques
Mesh-based reconstruction

## Slide 13: Shape from Silhouette
Binary images
Back project each silhouette  3D cone.
Carve all voxels outside the cone.
Result:
  Reconstruction contains the true scene, but not the same (no concavities)
  Not photo-consistent (only to binary images).
  In the limit reconstructs a visual hull
[Martin PAMI 91][Szeliski 93] + Our capgui in lab

## Slide 14: Smarter volumetric representations
Inaccurate
+ Triangulate w. marching cubes
+ Accurate
Franco, Boyer
+ Moderatly accurate
+ Fast
+ Marching intersections
Tarini’01 + our Capgui
Voxel-based Image ray based Axis-aligned

## Slide 15: Volumetric reconstruction
Method : Carve voxels that are not consistent with images (according to a chosen photo-consistency score).
OR
Assign colors to voxels consistent with the input images.
(color + opacity)
N3 voxels
C colors
all scenes
Photo-consist.
scenes
True scene
Not unique solution
Order of traversal v. important

## Slide 16: Voxel coloring
Each voxel
  Project in images and correlate
  Color if consistent
Visibility !
Depth ordering : Single visibility ordering for each view
(Restriction in camera placement)
Traversal
order
[Seitz,Dyer CVPR97]
Plane sweep [Collins CVPR 96]
No scene point contained within the convex hull of the cameras

## Slide 17: Voxel coloring : results
Input image
Results
[Seitz,Dyer CVPR97]

## Slide 18: Space carving
In general a view independent order might not exist
Space carving [Kutulakos, Seitz ICCV 99, IJCV 2002]
initialize a volume containing the scene
Choose a voxel on the surface of the scene
Project in all visible images
Carve if not consistent
Repeat until convergence
Consistency:
The resulting shape is photo-consistent
(all inconsistent voxels are removed)
Convergence:
Carving converges to a non-empty shape
(a point on the true surface is never removed)
Photo-hull

## Slide 19: Space carving : photo hull
Initial volume and
true scene
Photo-hull
Photo-hull = union of all photo-consistent shapes
Basic algorithm : requires a difficult update procedure (visibility computation after carving a voxel)
Multi-pass plane sweep :
Sweep plane in each 6 directions
Consider active only cameras on one side of the plane

## Slide 20: Space carving : results
[Kutulakos, Seitz ICCV 99, IJCV 2002]

## Slide 21: Graph cuts for multi-view reconstruction
Discrete surface reconstruction
Graph cut
Graph cuts as hypersurfaces
  Example: [Paris, Sillion, Quan IJCV 05]
Types of energies minimized with graph cut
[Kolmogorov Zabih ECCV 2002]
Graph cuts for multi-labeling

## Slide 22: Reconstruction as labeling
Discrete formulation:
surface representation
labels
Find a set of labels that minimize
Ex: disparity map voxels
pixels voxels
disparities occupancy
Notes:
NP hard
Can be solved using MRF energy minimization methods
  graph cuts (submodular E), dynamic programming, belief propagation,
  simulated annealing …
Photo-consistency
Smoothness

## Slide 23: Graph cuts
Oriented graph
  nodes
  edges
V , source s , sink t
E , edge capacity w(p,q)
(non-negative)
Cut C={S,T} partition of nodes into two disjoint sets such that sS, t T
Cost of the cut
Minimum cut cut that has minimum cost among all cuts (binary labeling)
Maximum flow maximum amount of liquid that can be sent from the source to the sink interpreting edges as pipes with capacity w.
Polynomial time algorithms
Augmenting paths [Ford & Fulkerson, 1962]
Push-relabel [Goldberg-Tarjan, 1986]

## Slide 24: Energy minimization via graph cuts
Motivation:
Geometric interpretation
cut = hypersurface in N-D space embedding the corresponding graph
used to compute optimal hypersurface
Powerful energy minimization tool for a large class of binary and non-binary energies
global minimum; strong local minimum
Surface reconstruction:
Chose a surface representation
Define a graph (nodes, weights) such that the cost of a cut corresponds to the surface energy function.
How to find global labeling using graph cut ?
What kind of energy can be minimized with a graph cut ?

## Slide 25: Graph Cuts as Hypersurfaces
s
t
cut
p
“cut”
x
y
labels
Graph fully embedded in the working geometric space
Feasible cut = separated hypersurface in the embedding continuous manifold

## Slide 26: Comparison to “stereo”
26
Multi-scanline optimization
L(p)
p
“cut”
x
y
labels
labels
x
L(p)
p
single scan line optimization
eg Search, Dynamic Programming
s-t Graph Cuts
multi-scan-line optimization

## Slide 27: Example of geometric graph
Disparity map: pixel label = disparity
[Paris, Sillion, Quan: A surface reconstruction method using global graph cut optimization IJCV 05]
source
sink
d1
d3
D1(d1)
d2
d4
D4(d1)
D3(d2)
D4(d2)
D4(d3)
D4(d4)
D2(d2)
D1(d2)
’
’
’
’
’
’




Graph
Surface
f1=d4
f2=d3
f3=d3
f4=d4

## Slide 28: Results
Convex smoothing – global solution
[Paris, Sillion, Quan IJCV 05, ACCV 04]

## Slide 29: Types of regularization energies
Convex
+ global convergence
oversmooth
V(Δf)
Δf=fp-fq
Potts
piecewise planar
binary graph
Preserves discontinuities
NP hard
? convergence
V(Δf)
Δf=fp-fq
V(Δf)
Δf=fp-fq
linear
Potts

## Slide 30: Graph cuts : state of the art
Optimization of first-order properties of segmentation boundary (Riemannian length/area, flux of a vector field)
Can’t optimize curvature of the boundary (for now)
Class of energies that can be minimized exactly
  binary energies with regular (sub-modular) interactions
  multi-label (non-binary) energies with “convex” interactions
    excludes robust discontinuity-preserving interactions
Guaranteed quality approximation algorithms for multi-label energies with discontinuity-preserving interactions…
  Potts model of interactions
  Metric interactions
  Regular (sub-modular) interactions
[ Boykov CVPR 05 Tutorial]

## Slide 31: GOTO slide 41

## Slide 32: Exact multi-labeling
Linear and convex smoothing (interaction) energy
Geometric graphs.
s
t
Multi-scan-line stereo
  [Roy & Cox 1998, 1999]
  [Ishikawa & Geiger 1999] (occlusion handling)
“Linear” interaction energy
  [Ishikawa & Geiger 1998]
  [Boykov, Veksler, Zabih 1998]
Convex interaction energy
  [Ishikawa 2000, 2003]

## Slide 33: Binary graphs
[Kolmogorov, Zabih : What energy functions can be minimized via graph cuts? ECCV 2002]
Complete characterization of energies that can be minimized with graph cut :
E(f) can be minimized by
s-t graph cuts
n-links
s
t
a cut
t-link
t-link
Large class of energies (Potts, metric …)
BUT multi-view reconstruction is a multi-labeling problem !

## Slide 34: Approximate multi-labeling
Binary Potts energy
Extended to multi-labeling
NP hard ( 3 labels)
n-links
s
t
cut
t-link
t-link
current
label
a
[ Boykov et al: Fast approximate energy via graph cuts, PAMI 2001]
Expansion approximate solution
Ideea: break optimization into a set of binary s-t cut problems
Each iteration – consider one label a
Binary cut: some labels are relabeled with a; the others remain unchanged

## Slide 35:  - expansion
initial labeling standard move swap a-expansion
Examples of standard and large moves from a given iniotia; labeling.
The number of labels is |L| = 3.

## Slide 36:  expansion
Properties
Guaranteed approximation quality
  within a factor of 2 from the global minima (Potts model)
Applies to a wide class of energies with robust interactions
  Potts model
  “Metric” interactions
  “Submodular” (regular) interactions
simulated annealing,
19 hours, 20.3% err
a-expansions (BVZ 89,01)
90 seconds, 5.8% err
normalized correlation,
start for annealing, 24.7% err

## Slide 37: Graph cut Example
[ Vogiatzis, Hermandez-Esteban, Torr, Cipolla PAMI 2007, CVPR 2005 ]
Surface representation: voxels; no need for bounding inner/outer surface
Regularization : weighted volume – balloon force
Minimization : graph cut
Occlusions : accounted using a voting photo-consistency score (occluded pixels are treated as outliers)
S = surface
V(S) = foreground
Photoconsistency
Foreground/background cost
(x)=-λ balloon force
silhouette cue – make (x) very large outside VH

## Slide 38: Photo-consistency metric
Account occlusions ρ(x,S) [continuous, level set formulations]
S determines visibility but S is the solution!
Problem : Not suitable for graph-cut
Solution : ρ(x) that accounts for occlusions using NCC
x
Optic ray
Correlation scores
Vote
ci
d

## Slide 39: Account occlusions

## Slide 40: Graph structure
Data (photo-consistency)
Ballooning
6 neighboring system

## Slide 41: Results
Vogiatzis2 0.50mm
Furukawa2 0.54mm

## Slide 42: Competitor – Yasu Furukawa 
Video

## Slide 43: Multi-view stereo
Disparity map
Depth w.r.plane
Level sets
Mesh
Voxels
Discrete
methods
Graph-cuts
Belief propagation
Dynamic programming…
Voxel carving (coloring)
Continuous
methods
Non-linear optimization
Variational calculus

## Slide 44: Continuous multi-view methods
Regular surface and surface evolution
Level set methods
Example of mesh-based reconstruction

## Slide 45: Surface evolution
Continuous formulation
recover shape (surface) by minimizing cost functional integrated over the surface.
Cost functional : photo-consistency + regularization (smoothness)
Numerical methods: gradient descent, conjugate gradient, level sets …
Natural extension of curve evolution (2D) [Caselles ICCV95] to 3D
[Robert,Deriche ECCV 96][Faugeras Kerivan 98]

## Slide 46: Regular surface = smooth
Definition: Regular surface (manifold)
is a regular surface if for each point there exist a neighborhood V and a map of an open set such that (X = parametrization):
X differentiable
X homeomorphism ( continuous)
the differentiable is one to one

## Slide 47: Regular surface - properties
Regular surface S
tangent vector
normal
area
curvature

## Slide 48: Surface evolution
Cost functional
Energy of the surface
Evolution flow (Euler-Lagrange equations)
OBS:
problem is intrinsic (independent on parameterization)
automatic regularization H
motion in the normal direction
whole surface is evolving in time (reference frame attached to the object)
1. Discretization
2. Choice of cost functional

## Slide 49: Photo-consistency functional
X
u
I
Image point u π(X)
Surface point X(u)=π-1(u,S) X
On Image On surface
π-1(u,S)
S-surface,
f(X)-color (radiance) of X
π(X)
Image i:

## Slide 50: Where to integrate image/surface ?
On Image On surface
Constant f
Impossible to reconstruct
2.Automatic regularization
1.Depends on image derivative
3.Doesn’t account for image discretization

## Slide 51: Surface evolution example
[Faugeras Kerivan 98]

## Slide 52: Modeling correct visibility
C
C’
[Gargallo et al ICCV 07]
Horizon term
Usual term
Heaviside func.
Dirac func.

## Slide 53: Surface discretization
Depth / disparity map
Image plane
3D point
Explicit representation
[Robert and Deriche: Dense depth recovery from stereo images, ECAI1992]
[Strecha et al: Dense matching of multiple wide-baseline views ICCV 2003]
Depth with respect to plane
3D plane
[Birkbeck et al 2006]
(Euler-Lagrange eq.)
Mesh
Move points along displacement direction
[Fua and Leclerc 1993]
[Birkbeck et al ECCV 2006]

## Slide 54: Level set representation
Surface = Zero level set of a higher dimensional function
[Osher and Sethian 88]
[Faugeras Keriven 98] (stereo)
[Soatto Yezzi Jin ICCV 03] (specular refl.)
normal
curvature
Evolution cost function
If
then
Efficient numerical schemes
[Sethian 96][Osher 02]
[Birkbeck]
Implicit representation

## Slide 55: Cost functional
Regularization : linear
quadratic + improves convergence
- penalizes large variation
- over-smoothing
non-quadratic, anisotropic
[Robert, Deriche 96] [Alvarez, Deriche 00] [Strecha 02]
(ex. Nagel-Enkelmann diff. oper.)
+ preserves discontinuities
Photo-consistency : image cues (SFS,PS,stereo,silhouette)
Where to integrate? : surface + makes the problem intrinsec
+ automatic regularization (multiplicative)
- over-smoothing
- not account for image discretization
image + can add a regularizer

## Slide 56: Goto p 66

## Slide 57: Surface/depth regularization
Depth map regularization f
1. Homogenous
Diffusion (heat eq)
2. Image-based regularization –
align depth discontinuities with the image discontinuities
3. Depth map regularization
Not smooth across surface discontinuities
energy
Euler Lagrange eq.
g – decreasing function g(s2)->0 when s big (high gradients) – inhibit diffusion
D – tensor
D

## Slide 58: Example regularization
Image-based regularization
correlation
i-b regul.
homog
Depth based
depth-based regularization

## Slide 59: Example regularization
i-b regul.
d-b regul

## Slide 60: Learn more about variational methods
Jan Erik Solem
PhD thesis,
Malmo Univ.
Level Set Methods
S. Osher and R. Fedkiw,
Springer 2003
Mathematical Problems in Image Processing
Aubert et al
Springer 2002
Hailin Jin
PhD thesis,
Washington Univ.
The Handbook of Mathematical Models in Computer Vision
N. Pragios editor
Springer 2005

## Slide 61: Graph-cuts and hypersurfaces
Geometric graph for stereo
Convex smoothing – global convergence
[Ishikawa, Geiger ECCV 1998]
[Roy,Cox ICCV 98, IJCV 1999]
Connection between cuts and hypersurfaces in continuous spaces
[ Boykov, Kolmogorov: Computing geodesics and minimal surfaces via graph cuts, ICCV 2003]
Show how to build a grid graph and sets the weights such that the cost of cuts is arbitrarily close to the area of corresponding surface for any anisotropic Riemannian metric.
Graph cut to find globally minimum surfaces (like level sets) under arbitrary Riemannian metric.
Riemannian metric (varying tensor)
Euclidian metric (ct)
A
B
distance
map
A
B
distance
map

## Slide 62: Minimal surfaces and graph cut
Riemannian metric (varying tensor)
Euclidian metric (ct)
A
B
distance
map
A
B
distance
map
Can the minimal surface energy be minimized with graph cut ?
[Boykov, Kolmogorov ICCV03,05]
multi view stereo formulation

## Slide 63: Cost of a cut
C
Cut metric is determined by the graph topology and by edge weights.
Cost of a cut can be interpreted as a geometric “length” (in 2D) or “area” (in 3D) of the corresponding contour/surface.

## Slide 64: Riemanian metric
Euclidean length of C
Cauchy-Crofton formula
the number of times
line L intersects C
C

## Slide 65
Cut Metric on grids can approximate Euclidean Metric
C
Euclidean
length
graph cut cost
for edge weights:
the number of edges of family k intersecting C
Edges of any regular neighborhood system generate families of lines
{ , , , }
Graph nodes are imbedded
in R2 in a grid-like fashion
8-neighborhoods
4-neighborhoods
(Manhattan metric)

## Slide 66: Example [Boykov]

## Slide 67: Summary: representations
Image centered
Depth/disparity map
Object centered
Implicit (level sets) Mesh Voxels
Image plane
3D point
+ | Natural extension of SFS, PS, stereo Strong min with graph cuts | Handles topological changes Implied normals Visibility | Graphics based Implied normals Visibility | Handles large structures Arbitrary topology
- | Limited resolution Partial obj. reconstr Viewpoint dependent | Too smooth Slow Closed surfaces | Topological changes | Ignores regularization (sensitive to noise) Limited resolution Occlusion handling
time

## Slide 68: Discrete vs. continuous
Level Sets | Graph Cuts
variational optimization method for fairly general continuous energies | combinatorial optimization for a restricted class of energies [e.g. KZ’02]
finds a local minimum near given initial solution | finds a global minimum for a given set of boundary conditions
numerical stability has to be carefully addressed [Osher&Sethian’88] continuous formulation -> “finite differences” | numerical stability is not an issue discrete formulation ->min-cut algorithms
anisotropic metrics are harder to deal with (e.g. slower) | anisotropic Riemannian metrics are as easy as isotropic ones
Gradient descent method VS. Global minimization tool
(restricted class of energies)
[Boykov CVPRTut 2005]

## Slide 69: A complete system
Neil Birkbeck
Motivation
method that works for objects with general reflectance
  textured and uniform regions shading + texture
        light variation (multiview PS)
  specular materials general BRDF – parametric
System
Camera calibration: pattern
Light calibration: specular white sphere
Light variation: rotating table, fixed cam.

## Slide 70: Cost functional
Cost functional
camera proj.
image
light
Per-point cost function
Visibility+sampling
reflectance
1. Lambertial reflectance
light color
light dir.
ambient color
BRDFalbedo
2. Non-Lambertian reflectance
BRDF = Phong
In practice : filter specular highlights
fit full reflectance only at the end

## Slide 71: Surface discretization
Surface = triangles,
move vertices
Normals interpolated
Albedo implied by the shape (closed form solution)
(knowing light dir+color)
Visibility/shadows Z buffering
Cost function

## Slide 72: Surface discretization
Regularizer mean curvature
Gradient finite differences
Multi-resolution (image pyramid)
Mesh handles topological changes
Initial shape = visual hull

## Slide 73: Results : refinement

## Slide 74: Results : shape + reflectance

## Slide 75: Improvements
Better light model – no need for calibration
Model background ? no need to extract silhouette (foreground) – Mumford-Shah functional
Discontinuities – anisotropic regularization; discontinuous mesh
Incorporate noise ?

## Slide 76: Capture system
Shape from silhouette
Dynamic texture