## Slide 1: CMPUT 399 Intro Robotics & Mechatronics: Control
Masood Dehghan
Sep. 2019
with slides from Chad Jenkins (U Michigan) and Oussama Khatib (Stanford)

## Slide 2: Outline
Control
  2nd Order ODEs
  Natural (passive) systems
  PID Control

## Slide 3: Motivation
Control >>> design the behavior of your mechatronic system.
Boston Dynamics' Atlas robot can backflip now

## Slide 4: Natural (passive) systems
Mass-spring system 2nd order system:
  Newton's Law: F = m.a
https://www.myphysicslab.com/springs/single-spring-en.html
Normalized

## Slide 5: Dissipative systems
Dissipative systems
Normalized:

## Slide 6: 2nd order system
Higher ω : faster response
Higher : slower response
= 1 : optimal choice
https://www.myphysicslab.com/springs/single-spring-en.html

## Slide 7: 2nd order system
Higher ω : faster response
Higher : slower response
= 1 : optimal choice
https://www.myphysicslab.com/springs/single-spring-en.html

## Slide 8: 2nd order systems are Practical
https://codepen.io/dissimulate/pen/KrAwx
Cool animation with multiple spring-dampers:
Control >>> Design how your system behave.

## Slide 9: Use Control to make robots behave like a dissipative system
PD – control
Proportional + Derivative
: goal of controller is to move robot to xd
robot
input
output
f (xd , x)
x
Change behavior with kp , kd

## Slide 10: Control Systems
Overall block diagram
  System (+actuator)
  Feedback (sensors)
  Controller (design)
Control Methods:
  Model-based
    Requires an approximate (linear / nonlinear) model of system.
    Uncertainties (un-modeled dynamics) are modeled as disturbance
  Model-free
    Learning-based approaches, e.g. RL , adaptive, etc.

## Slide 11: PID control Proportional + Integral + Derivative
PID:
  simple, easy to implement, practical, model-free
  need heuristics for tuning the gains
Proportional + Integral + Derivative Control

## Slide 12: PID control Proportional + Integral + Derivative
Proportional + Integral + Derivative Control
P term is proportional to the current value
I term accounts for past values
D term is a best estimate of the future trend
Based on mass-spring-damper system

## Slide 13: PID control
e(t) = xd(t) -x(t)

## Slide 14: PID control
Proportional + Integral + Derivative Control
[wikipedia: PID control]

## Slide 15: PID: digital implementation
Discrete integral
Derivative (backward finite difference)
Pseudocode

## Slide 16: PID gain tuning
Start will all gains at zero: Kp=Kd=Ki=0
Increase Kp until system roughly meets desirable state
  Overshoot & oscillation are acceptable
Increase Kd until system is stable
Increase Ki until system consistently reaches xd
Refine gains to improve performance
Will test this in lab 2, for Lego actuators

## Slide 17: Tracking Control
What if we want to track a trajectory, i.e. xd is changing with time: xd(t)

## Slide 18: Motivation
Control >> Design how your mechatronic system behave.

## Slide 19: Control of Nonlinear Systems

## Slide 20: Disturbance Rejection

## Slide 22: Practical issues for choosing Controller Gains
Rule of thumb:
ω = (3 to 10 Hz)*2π
ζ = 1
Tacoma Narrows Bridge (1940)