## Slide 1: CMPUT 399 Intro Robotics & Mechatronics: Motor Control
Some slides are taken from Northwestern University’s “ME 333 Introduction to Mechatronics” by Kevin Lynch.

## Slide 2: DC motors
DC motors: cheap, most common
DC motor ?
https://www.youtube.com/watch?v=LAtPHANEfQo

## Slide 3: Brushed permanent magnet DC motor
Lorentz’ law: F = l I x B
  current flowing through a magnetic field creates a force on the wire carrying the current
Torque changes direction
- switch direction of current
- still torque varies
- use 3 loops
- still have torque ripple
- insufficient torque > use coil instead of wire
- commutators to switch current

## Slide 4: Model of DC motor Control
kt : torque constant : characteristic of motor
V
I
𝜏,⍵
back-emf (electro-motive force) voltage
Opposing the driving voltage
Mechanical power (output)
(friction loss, heating, etc.)
Open-circuit: I=0
Electrical power (input)

## Slide 5: Speed-Torque curve
⍵0: no-load speed
𝜏s: prevent moving ⇒ large torque (𝜏=kt I) ⇒
large current ⇒ (Power=RI2)⇒ overheating (over long period of time)
0
nominal operating point
nominal mechanical power
continuous operating region
Speed-Torque curve

## Slide 6: Mechanical power in speed-torque curve
Efficiency = = x 100 %

## Slide 7: Mechanical power in speed-torque curve
Efficiency = = x 100 %

## Slide 8: Motor specification (datasheet)

## Slide 9: DC motor control
Goal: drive a DC motor with micro-controller
Vm
𝜏,⍵
M
dig. out
Low voltage
Low current
Add a switch
Large change of current ⇒ sparks
use diode (flyback diode)
current decay to zero exponentially
enable us to turn motor on/off
+V
dig. out
M
⏄
to control speed we use PWM
PWM controls duty cycle of closing/opening the switch
10 KHz < f < 40 KHz
enable us to control speed in 1-direction
bi-directional >>> H-bridge

## Slide 10: DC motor control
H-bridge
closed switches:
S1 , S4 : forward
S2 , S3 : reverse
S1 , S3 : brake
S2 , S4 : brake
one/none: coast
OUT1 OUT2
off off coast
H L forward
L H reverse
shorted brake

## Slide 11: Motor Control System
Complete motor control system
ref
position
(θd)
Motion controller
PI
controller
H-bridge
motor
current sensor
counter
encoder
torque /
Current
command
𝝨
current
error
20 KHz
PWM duty
current
measured
position
measured
current
+
_
PID
5 KHz
inner loop
200-1000 Hz
outer loop

## Slide 12: BLDC motors
Brushless DC (BLDC) motor :
https://www.youtube.com/watch?v=bCEiOnuODac