## Slide 1: Using 2D projective geometry to control of robot motion from video “visual servoing”
M. Jagersand

## Slide 2: What is vision?
Two main categories
Object recognition: Use cues in 2D image
Spatial vision: Understand and invert the 3D to 2D imaging process: Two subcategories:
  Full 3D scene reconstruction
  Use of partial 3D information, implicitly or explicitly

## Slide 3: Uses of partial information from 2D-3D camera geometry
Single view measurements
Visual constraints: verify alignments, detect impossible configurations (Esher paintings)
Visual servoing
  Lukas Kanade –like
  Deep Learning
Visual tracking
  Features instead of images
… many more

## Slide 4: Geometric Cues
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 5: Estimating Height
The distance || tr – br || is known
Used to estimate the height of the man in the scene

## Slide 6: Vision-Based Control (Visual Servoing)
Initial Image
Desired Image
User

## Slide 7: Vision-Based Control (Visual Servoing)
: Current Image Features
: Desired Image Features

## Slide 8: Vision-Based Control (Visual Servoing)
: Current Image Features
: Desired Image Features

## Slide 9: Vision-Based Control (Visual Servoing)
: Current Image Features
: Desired Image Features

## Slide 10: Vision-Based Control (Visual Servoing)
: Current Image Features
: Desired Image Features

## Slide 11: Vision-Based Control (Visual Servoing)
: Current Image Features
: Desired Image Features

## Slide 12: u,v Image-Space Error
: Current Image Features
: Desired Image Features
One point
Pixel coord
Many points
u
v
Notes: Error vectors in image space -> composed total error vector

## Slide 13: Conventional Robotics: Motion command in base coord
We focus on the geometric transforms
EE

## Slide 14: Problem: Lots of coordinate frames to calibrate
Camera
  Center of projection
  Different models
Robot
  Base frame
  End-effector frame
  Object

## Slide 15: Image Formation is Nonlinear
Camera
frame

## Slide 16: Camera Motion to Feature Motion
Camera
frame

## Slide 17: Camera Motion to Feature Motion
Interaction matrix is a Jacobian.
This derivation is
for one point.
Q. How to extend
to more points?
Q. How many
points needed?
Notes: Needs a-priori f and Z

## Slide 18: Problem: Lots of coordinate frames to calibrate
Camera
  Center of projection
  Different models
Robot
  Base frame
  End-effector frame
  Object
Only covered one transform!

## Slide 19: Other (easier) solution: Image-based motion control
Motor-Visual function: y=f(x)
Achieving 3d tasks
via
2d image control
Notes: Use notes: Motivation from motion estimation.

## Slide 20: Other (easier) solution: Image-based motion control
Motor-Visual function: y=f(x)
Achieving 3d tasks
via
2d image control
Note: What follows will work for one or two (or 3..n) cameras. Either fixed or on the robot.
Here we will use two cam

## Slide 21: Simplest case: 2D planar world and aligned camera
This method is commonly used in industry machine vision
  Usually overhead camera pointing straight down on a work table
  Adjust cam position so pixel [u,v] = s[X,Y]. s = scalefactor (pix/mm)
  Pixel coordinates are scaled world coord
X
Y
u
v
Camera
Robot scene
Thresholded image

## Slide 22: My first robotics problem

## Slide 23: Vision-Based Control
Image 1
Image 2

## Slide 24: Vision-Based Control
Image 1
Image 2

## Slide 25: Vision-Based Control
Image 1
Image 2

## Slide 26: Vision-Based Control
Image 1
Image 2

## Slide 27: Vision-Based Control
Image 1
Image 2

## Slide 28: Image-based Visual Servoing
Observed features:
Motor joint angles:
Local linear model:
Visual servoing steps: 1 Solve:
2 Update:

## Slide 29: Find J Method 1: Test movements along basis
Remember: J is unknown m by n matrix
Motor moves (scale these):
Suitable
Finite difference:

## Slide 30: Find J Method 2: Secant Constraints
Constraint along a line:
Defines m equations
Collect n arbitrary, but different measures y
Solve for J

## Slide 31: Find J Method 3: Recursive Secant Constraints
Based on initial J and one measure pair
Adjust J s.t.
Rank 1 update:
Consider rotated coordinates:
  Update same as finite difference for n orthogonal moves

## Slide 32: Achieving visual goals: Uncalibrated Visual Servoing
Solve for motion:
Move robot joints:
Read actual visual move
Update Jacobian:
repeat

## Slide 33: Achieving visual goals: Uncalibrated Visual Servoing
Solve for motion:
Move robot joints:
Read actual visual move
Update Jacobian:
repeat
Can we always guarantee when a task is achieved/achievable?

## Slide 34: What we need for VS
Camera(s) Place for visibility and
Tracking
  Markerless algorithms - MTF
  Put LED on robot end-effector
    Lower brightness so LED brighterest
Robot: Anywhere within reach
Control command access
  Joint posiiton move
  Joint velocity
  Cartesian
    Issues with angle representation: Euler, quatern, exp
LED
Camera
X
Y
u
v

## Slide 35: Visually guided motion control
Issues:
What tasks can be performed?
  Camera models, geometry, visual encodings
How to do vision guided movement?
  H-E transform estimation, feedback, feedforward motion control
How to plan, decompose and perform whole tasks?

## Slide 36: How to specify a visual task?

## Slide 37: Task and Image Specifications
Task function T(x) = 0 Image encoding E(y) =0
task space error
image space error
image space satisfied
task space satisfied

## Slide 38: Visual specifications
Point to Point task “error”:
Why 16 elements?

## Slide 39: Visual specifications 2
Point to Line
Line:
Note: y homogeneous coord.

## Slide 40: Parallel Composition example
E (y ) =
wrench
y - y
4
7
y - y
2
5
y • (y  y )
8
3
4
y • (y  y )
6
1
2
(plus e.p. checks)

## Slide 41: How to define a visual task?

## Slide 42: 5.4. Visual specifications
Image commands = Geometric constraints in image space
HRI: User points/clicks on features in an image
Robot controller drives visual error to zero

## Slide 43: Visually defined alignment: basic
point-to-point: epp(y) = y2 - y1
point-to-line: epl(y) = y1 . (y2 x y3)
or (homogenous coord) epp(y) = y2 x y1

## Slide 44: Some more visual alignments
parallel lines: epar(l) = (l1 x l2) x (l3 x l4)
point-to-ellipse: epe(y) = yT1 Cellipse y1
line-to-line: ell(y) = y1 . (y3 x y4) + y2 . (y3 x y4)

## Slide 45: Now: Language for visual alignments What else do we need?
Registration
trackers:
Feature
trackers
Need: 1. Some way of entering alignments in images 2. video tracking to perform servoing!
Download:
http://webdocs.cs.ualberta.ca/~vis/mtf/

## Slide 46: ViTa: Visual Task spec. for Manip. Mona Gridseth, Martin Jagersand ICRA’16

## Slide 47: Composing basic visual alignments 1. Parallel
Which encoding E(y) is better? Can both reach E(y) = 0 ?
Do we need 1 or 2 cameras? Why?
E (y ) =
wrench
y - y
4
7
y - y
2
5
y • (y  y )
8
3
4
y • (y  y )
6
1
2
Conceptual task
Image of task

## Slide 48: Composing basic visual alignments 1. Parallel constrains

## Slide 49: Composing basic visual alignments 2. Serial seqencing
Many tasks divide naturally into
Transportation / reaching
  Coarse primitive for large movements
  Low DOF control (e.g. of object centroid)
  Robust to disturbances
Fine Manipulation
  For high precision control of both position and orientation
  6DOF control based on several object features

## Slide 50: Serial Composition Solving whole real tasks
Linked task primitive
Acceptable initial (visual) conditions
Visual or Motor constraints to be maintained
Final desired condition
Task =

## Slide 51: Previous alignments just examples. Can use any invariants for the level of calibration available
Group | Transformation | Invariants | Distortion
Projective 8 DOF |  | Cross ratio Intersection Tangency | 
Affine 6 DOF |  | Parallelism Relative dist in 1d Line at infinity | 
Metric 4 DOF |  | Relative distances Angles Dual conic | 
Euclidean 3 DOF |  | Lengths Areas | 
¥
C*
2 dof
¥
l
2 dof
¥
l
¥
C*

## Slide 52: Achieving visual goals: Uncalibrated Visual Servoing
Solve for motion:
Move robot joints:
Read actual visual move
Update Jacobian:
repeat
Can we always guarantee when a task is achieved/achievable?

## Slide 53: Task ambiguity
Will the scissors cut the paper in the middle?

## Slide 54: Task ambiguity
Will the scissors cut the paper in the middle? NO!

## Slide 55: Task Ambiguity
Is the probe contacting the wire?

## Slide 56: Task Ambiguity
Is the probe contacting the wire? NO!

## Slide 57: Task Ambiguity
Is the probe contacting the wire?

## Slide 58: Task Ambiguity
Is the probe contacting the wire? NO!

## Slide 59: Task decidability and invariance
A task T(f)=0 is invariant under a group G of transformations, iff
x
 f  V , g  G with g(f )  V T(f )=0  T(g(f ))=0
n
x
n
If T(f ) = 0 here,
T(f ) must be 0 here, if T is G invariant
T(f ) must be 0 here, if T is G invariant
T(f ) must be 0 here, if T is G invariant
T(f ) must be 0 here, if T is G invariant
proj
inj
sim
aff

## Slide 60
All achievable tasks...
are ALL projectively distinguishable coordinate systems
One point
Coincidence
Noncoincidence
1
0
0
0
1
0
0
0
1
0
0
0
1
0
0
0
0
1
0
0
1
0
0
0
1
0
0
0
1
0
0
0
1
0
0
0
1
0
0
0
0
1
0
0
1
0
0
0
0
1
0
0
0
0
1
0
Collinearity
General Position
2pt. coincidence
3pt. coincidence
1
0
0
0
0
1
0
0
1
1
0
0
1
0
0
0
1
0
0
0
1
0
0
0
1
0
0
0
1
0
0
0
1
0
0
0
0
1
0
0
0
1
0
0
1
0
0
0
0
1
0
0
1
1
0
0

1
0
0
1
0
0
0
0
1
0
0
0
0
1
0
1
1
1
0
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
4pt. coincidence
2 2pt. coincidence
Cross Ratio
General Position
Coplanarity

## Slide 61
Tpp
Tcol
Tcopl
Tcr
point-coincidence
collinearity
coplanarity
cross ratios (a)
Cinj
Cwk
Task primitives
Tpp
Injective
Projective
Composing possible tasks
Task operators
T1  T2 =
T1  T2 = T1•T2
T =
0 if T = 0
1 otherwise
T1
T2
AND
OR
NOT

## Slide 62
wrench: view 1
wrench: view 2
Twrench(x1..8) =
Tcol(x2,x5,x6)
Tcol(x4,x7,x8) 
Tpp(x1,x5) 
Tpp(x3,x7) 
1
2
3
4
5
6
7
8
Result: Task toolkit

## Slide 63: Example: Pick and place type of movement
3. Alignment???
  To match transport final to fine manipulation initial conditions

## Slide 64: More primitives
4. Guarded move
  Move along some direction until an external contraint (e.g. contact) is satisfied.
5. Open loop movements:
  When object is obscured
  Or ballistic fast movements
  Note can be done based on previously estimated Jacobians

## Slide 65: Solving the puzzle…

## Slide 66: Conclusions
Visual servoing: The process of minimizing a visually-specified task by using visual feedback for motion control of a robot.
Is it difficult? Yes.
  Controlling 6D pose of the end-effector from 2D image features.
  Nonlinear projection, degenerate features, etc.
Is it important? Of course.
  Vision is a versatile sensor.
  Many applications: industrial, health, service, space, humanoids, etc.

## Slide 67: What environments and tasks are of interest?
Not the previous examples.
  Could be solved “structured”
Want to work in everyday unstructured environments

## Slide 68: Use in space applications
Space station
On-orbit service
Planetary Exploration

## Slide 69: Power line inspection
Model landscape: Edmonton railroad society
A electric UAV carrying camera flown over the model
Simulation: Robot arm holds camera

## Slide 70: Use in Power Line Inspection
Notes: spanish (project colobri U madrid), wales: Jones,
Photosynth some power poles.
Q: How close must illustrating examples be?
Only power lines? Or other CV capture?

## Slide 71: Some References
M. Spong, S. Hutchinson, M. Vidyasagar. Robot Modeling and Control. Chapter 12: Vision-Based Control. John Wiley & Sons: USA, 2006. (Text)
S. Hutchinson, G. Hager, P. Corke, "A tutorial on visual servo control," IEEE Trans. on Robotics and Automation, October 1996, vol. 12, no 5, p. 651-670. (Tutorial)
F. Chaumette, S. Hutchinson, "Visual Servo Control, Part I: Basic Approaches," and "Part II: Advanced Approaches," IEEE Robotics and Automation Magazine 13(4):82-90, December 2006 and 14(1):109-118, March 2007. (Tutorial)
B. Espiau, F. Chaumette, P. Rives, "A new approach to visual servoing in robotics," IEEE Trans. on Robotics and Automation, June 1992, vol. 8, no. 6, p. 313-326. (Image-based)
W. J. Wilson, C. C. Williams Hulls, G. S. Bell, "Relative End-Effector Control Using Cartesian Position Based Visual Servoing", IEEE Transactions on Robotics and Automation, Vol. 12, No. 5, October 1996, pp.684-696. (Position-based)
E. Malis, F. Chaumette, S. Boudet, "2 1/2 D visual servoing," IEEE Trans. on Robotics and Automation, April 1999, vol. 15, no. 2, p. 238-250. (Hybrid)
M. Jägersand, O. Fuentes, R. Nelson, "Experimental Evaluation of Uncalibrated Visual Servoing for Precision Manipulation," Proc. IEEE Intl. Conference on Robotics and Automation (ICRA), pp. 2874-2880, 20-25 Apr. 1997. (Uncalibrated, model-free)
F. Chaumette, "Potential problems of stability and convergence in image-based and position-based visual servoing," The Confluence of Vision and Control, LNCS Series, No 237, Springer-Verlag, 1998, p. 66-78.