## Slide 1: Robot Arms, Hands:
With slides from

## Slide 2: What a robot arm and hand can do
Martin 1992-’97 PhD work

## Slide 3: What a robot arm and hand can do
Camilo 2011-15 PhD work

## Slide 4: Robotics field . .
6 Million mobile robots
  From $100 roomba to $millions Mars rovers
3 million robot arms
  Usually $20,000-100,000, some $millions (Canadaarm)
Value of industrial robotics sector: $100 billion
  Roomba: $300M in sales
  Industrial arms $75billion in sales
Arms crucial for these industries:
  Automotive (Welding, painting, some assembly)
  Electronics (Placing tiny components on PCB)
  General: Pack boxes, move parts from conveyor to machines
http://www.youtube.com/watch?v=DG6A1Bsi-lg

## Slide 5: 01_02
Chances are, something you eat, wear, or use was made by a robot
Robots in everyday use and popular culture
http://www.robotuprising.com/
Notes: 01_02.jpg

## Slide 6: Common applications
Industrial
  Robotic assembly
Commercial
  Household chores
Military
Medical
  Robot-assisted surgery
Picture of Roomba
Notes: Congressional act: more autonomous military vehicles/agents

## Slide 7: Common applications
Planetary Exploration
  Fast, Cheap, and Out of Control
  Mars rover
Undersea exploration
JHUROV; Johns Hopkins
Notes: Finding the titanic using the first underwater robot

## Slide 8: 01_01
Industrial robots
High precision and repetitive tasks
  Pick and place, painting, etc
Hazardous environments
Notes: Industrial robot movie. Use industrial robots as a basis for analysis.
01_01.jpg

## Slide 9: Emerging Robotics Applications
Space - in-orbit, repair and maintenance, planetary exploration anthropomorphic design facilitates collaboration with humans
Military or Hazardous - supply chain and logistics support, re-fueling, bomb disposal, toxic/radioactive cleanup
Health - clinical applications, "aging-in-place,” physical and cognitive prosthetics in assisted-living facilities
Basic Science - computational models of cognitive systems, task learning, human interfaces
No or few robots currently operate reliably in these areas!

## Slide 10: 01_03
Representations
For the majority of this class, we will consider robotic manipulators as open or closed chains of links and joints
  Two types of joints: revolute (q) and prismatic (d)
Notes: 01_03.jpg

## Slide 11: Definitions
End-effector/Tool
  Device that is in direct contact with the environment. Usually very task-specific
Configuration
  Complete specification of every point on a manipulator
  set of all possible configurations is the configuration space
  For rigid links, it is sufficient to specify the configuration space by the joint angles
State space
  Current configuration (joint positions q) and velocities
Work space
  The reachable space the tool can achieve
    Reachable workspace
    Dextrous workspace
Notes: Talk about the number of DOFs in terms of workspace reachability and redundancy. Rigid body has 6DOF

## Slide 12: 01_06
Common configurations: wrists
Many manipulators will be a sequential chain of links and joints forming the ‘arm’ with multiple DOFs concentrated at the ‘wrist’
Notes: 01_06.jpg

## Slide 13: 01_07
Example end-effector: Grippers
Anthropomorphic or task-specific
  Force control v. position control
Utah MIT hand
Notes: 01_07.jpg

## Slide 14: An classic arm - The PUMA 560
The PUMA 560 has SIX revolute joints
A revolute joint has ONE degree of freedom ( 1 DOF) that is defined by its angle
1
2
3
4
There are two more joints on the end effector (the gripper)

## Slide 15: An modern arm - The Barrett WAM
The WAM has SEVEN revolute joints.
Similar motion (Kinematics) to human

## Slide 16: UA Robotics Lab platform 2 arm mobile manipulator
2 WAM arms, steel cable transmission and drive
Segway mobile platform
2x Quad core computer platform.
Battery powered, 4h run time.

## Slide 17: Robotics challenges
Navigation ‘05
Manipulation ‘11-14
Humanoids ’12-

## Slide 18: Build or buy?
Off the shelf kits:
Build your own:
Lego
Lynxmotion

## Slide 19: Mathematical modeling
Strategy:
Model each joint separately
Combine joints and linkage lengths
Robot
Abstract model
http://www.societyofrobots.com/robot_arm_tutorial.shtml

## Slide 20: 01_09
Common configurations: elbow manipulator
Anthropomorphic arm: ABB IRB1400
Very similar to the lab arm (RRR)
Notes: 01_09.jpg

## Slide 21: 01_10
Workspace: elbow manipulator
Notes: 01_10.jpg

## Slide 22: 01_12
Common configurations: Stanford arm (RRP)
Spherical manipulator (workspace forms a set of concentric spheres)
Notes: 01_12.jpg

## Slide 23: 01_14
Common configurations: SCARA (RRP)
Adept Cobra Smart600 SCARA robot
Notes: 01_14.jpg

## Slide 24: 01_15
Common configurations: cylindrical robot (RPP)
Seiko RT3300 Robot
workspace forms a cylinder
Notes: 01_15.jpg

## Slide 25: 01_16
Common configurations: Cartesian robot (PPP)
Increased structural rigidity, higher precision
  Pick and place operations
Notes: 01_16.jpg

## Slide 26: 01_17
Workspace comparison
(a) spherical
(b) SCARA
(c) cylindrical
(d) Cartesian
Notes: 01_17.jpg

## Slide 27: Linkage configuration
Motors serially in arm
Each motor carries the weight of previous
Heavy
Motors at base
Lightweight and faster
More complex transmission
Pic of our small arm

## Slide 28: 01_18
ABB IRB940 Tricept
Parallel manipulators
6DOF Stewart platform
some of the links will form a closed chain with ground
Advantages:
  Motors can be proximal: less powerful, higher bandwidth, easier to control
Disadvantages:
  Generally less motion, kinematics can be challenging
ABB IRB6400
Notes: 01_18.jpg

## Slide 29: Hands, two arms: also parallel

## Slide 30: How to build your Lego robot
Minimize loading of motors from weight of other motors.
Solutions:
SCARA
Parallelogram linkage
(Similar to a Phantom 1)

## Slide 31: Mathematical modeling
Strategy:
Model each joint separately
Combine joints and linkage lengths
A simple example follows here.
More general treatment of next lecture
Robot
Abstract model
http://www.societyofrobots.com/robot_arm_tutorial.shtml

## Slide 32: 01_19
Simple example: Modeling of a 2DOF planar manipulator
Move from ‘home’ position and follow the path AB with a constant contact force F all using visual feedback
Notes: 01_19.jpg

## Slide 33: 01_20
Coordinate frames & forward kinematics
Three coordinate frames:
Positions:
Orientation of the tool frame:
0
1
2
0
1
2
Notes: ‘0’ is the base frame, ‘2’ is the tool frame. The orientation of the tool frame is the projection of the tool frame onto the base frame (i.e. dot product)
01_20.jpg

## Slide 34: 01_21
Inverse kinematics
Find the joint angles for a desired tool position
Two solutions!: elbow up and elbow down
Notes: These are simple examples… this becomes more complex for higher DOFs
01_21.jpg

## Slide 35: 01_23
State space includes velocity
Inverse of Jacobian gives the joint velocities:
This inverse does not exist when q2 = 0 or p, called singular configuration or singularity
Velocity kinematics: the Jacobian
Notes: Give an example of a human arm fully extended
01_23.jpg

## Slide 36: 01_24
Path planning
In general, move tool from position A to position B while avoiding singularities and collisions
  This generates a path in the work space which can be used to solve for joint angles as a function of time (usually polynomials)
  Many methods: e.g. potential fields
Can apply to mobile agents or a manipulator configuration
Notes: Potential fields: create a topological map of the environment to account for obstacles (i.e. obstacles would be surrounded by ‘high’ potential fields) and take the path of lowest energy
01_24.jpg

## Slide 37: 01_24
system dynamics
Joint control
Once a path is generated, we can create a desired tool path/velocity
  Use inverse kinematics and Jacobian to create desired joint trajectories
measured trajectory (w/ sensor noise)
error
controller
actual trajectory
desired trajectory
Notes: 01_24.jpg

## Slide 38: Other control methods
Force control or impedance control (or a hybrid of both)
  Requires force/torque sensor on the end-effector
Visual servoing
  Using visual cues to attain local or global pose information
Common controller architectures:
  PID
  Adaptive
  Repetitive
Challenges:
  Underactuation
  Nonholonomy (mobile agents)
  nonlinearity
Notes: We will form a matrix for both sensors and actuators to describe some common configurations as well as discuss active research in both these areas

## Slide 39: General multivariable control overview
desired trajectory
desired joint torques
state estimation sensors
inverse kinematics,
Jacobian
manipulator dynamics
joint controllers
motor dynamics
estimated configuration

## Slide 40: Sensors and actuators
sensors
  Motor encoders (internal)
  Inertial Measurement Units
  Vision (external)
  Contact and force sensors
motors/actuators
  Electromagnetic
  Pneumatic/hydraulic
  electroactive
    Electrostatic
    Piezoelectric
Basic quantities for both:
Bandwidth
Dynamic range
sensitivity
Notes: We will form a matrix for both sensors and actuators to describe some common configurations as well as discuss active research in both these areas

## Slide 41: Computer Vision
Simplest form: estimating the position and orientation of yourself or object in your environment using visual cues
  Usually a statistical process
  Ex: finding lines using the Hough space
More complex: guessing what the object in your environment are
Biomimetic computer vision: how do animals accomplish these tasks:
  Obstacle avoidance
    Optical flow?
  Object recognition
    Template matching?
Notes: Mention real-world problems such as cameras/calibration, lighting, etc

## Slide 42: MEMS and Microrobotics
Difficult definition(s):
  Robotic systems with feature sizes < 1mm
  Robotic systems dominated by micro-scale physics
MEMS: Micro ElectroMechanical Systems
  Modified IC processes to use ‘silicon as a mechanical material’
Pister; Berkeley
Donald; Dartmouth
Fearing; Berkeley

## Slide 43: Surgical robotics
Minimally invasive surgery
  Minimize trauma to the patient
  Potentially increase surgeon’s capabilities
  Force feedback necessary, tactile feedback desirable

## Slide 44: Humanoid robots
For robots to efficiently interact with humans, should they be anthropomorphic?
Asimo; Honda (video from Siegwart?)
QRIO Sony

## Slide 45: Winning IROS 2000-2012 work

## Slide 46: Next class…
Homogeneous transforms as the basis for forward and inverse kinematics
Consider reading:
Craig, J.J., Introduction to Robotics, Mechanics, and Control
Chapter 3 (and 2 if math/geometry review needed)
Book available in library, bookstore or on-line
Other texts:
M. Spong, S. Hutchinson, and M. Vidyasagar, “Robot Modeling and Control”, Wiley
(In UA library)
Grad level:
Li, Murray, Sastry, “A Mathematical Introduction to Robotic Manipulation”, CRC Press
(Downloadable PDF on-line@Caltech)